## Slide 1: Gold Mountain CSD February 25th 2021 Special Board Meeting Utility Rates & Fees Study
All Figures and Numbers shown are Subject to Change while the Study is being conducted
<number>

## Slide 2
Section I
Best Practices and California Law
<number>
Notes: <number>

## Slide 3: Fee Setting Process: Every 3-5 Years
<number>
Last GMCSD rate study in 2006 – 15 Years ago
Cost of service analysis also required with the rate study

## Slide 4: Purpose of the Study
Review of Financial Health & Practices – The CSD has never had a comprehensive review of its overall fiscal health and revenue collection policies and practices. The last rate study was conducted in 2006.
Revenue Sufficiency - Make sure sufficient money to operate the utilities for the next 5+ years to provide customers with adequate, clean, safe potable water and reliable wastewater disposal that meets State and Federal regulatory standards
CIP - Create adequate revenue for funding of capital improvement projects (CIP) for the water and wastewater systems
Meet Debt Covenants – There is no current debt; however, the rate study accounts for potential future debt and covenants it would carry
<number>

## Slide 5: District Financial Health
<number>
Financially healthy but drawing on reserves and several cost increases anticipated in next 5 years

## Slide 6: California Prop. 218 Requirements for RATES
Revenues from the fee shall not exceed funds required to provide the service.
Revenues from the fee shall not be used for any purpose other than that for which it was imposed.
The amount of the fee imposed as an incident of property ownership shall not exceed the proportional cost of service to the parcel.
No fee may be imposed for service unless the service is used OR is immediately available to the parcel.
No fee may be imposed for general governmental services (such as police, fire, library) where the service is available to the public at large in much the same manner as to the parcels charged the fee.
<number>

## Slide 7: Industry Standards and Principles
American Water Works Manual M1 – “Principles of Water Rates, Fees, and Charges”
Water Environment Federation Manual M27 – “Financing and Charges for Wastewater Systems”
Government Finance Officers Association – “Appropriate Levels of Working Capital in Enterprise Funds”
<number>

## Slide 8: Step 1: Revenue Requirement
Determine funding needed from rates to meet financial needs:
  Operations & Maintenance
  Debt Service
  System Rehabilitation
  Capital Improvements
  Prudent Reserves
<number>
Notes: Depreciation:
The accounting term for the cost of System Rehabilitation
Recovering the cost of an asset over its estimated lifetime
Different methods of calculation
Most widely used is a “straight-line”
<number>

## Slide 9: Step 2: Cost of Service
Allocation of the revenue requirement among customer groups to reflect proportionate cost/demands on the system
<number>

## Slide 10: Step 3: Rate Design
How to collect the necessary revenue requirement from customer groups
  Customer Charges
  Service Charges
  Use Charges
<number>
Notes: <number>

## Slide 11
Section II
Revenue Requirement
<number>
Notes: <number>

## Slide 12: Projected Revenue Requirement
Determines amount to be collected in rates
Operating Costs
  Increase about 5% per year
  Addition of Personnel costs in Year 1 (greater than the 5%)
  System Improvements
  Collection for depreciation (replacement of existing assets) @ 75%
New Debt [potential]
  Water Reclamation Plant (2023) – sewer fund
  High Elevation Tank (2025) – water fund
Less Credits
  Credits include connection fees, late charges, interest, and administrative fee revenues
<number>

## Slide 13: Capital Improvement Projects WATER SEWER
Improvements | Current $ | Inflated $
High Elevation Tank | $700,000 | $802,000
Well 29 Rehabilitation | $235,000 | $270,000
SCADA | $75,000 | $81,000
Booster Station #8 | $120,000 | $134,000
Well 36 Connections | $70,000 | $84,000
Various Upgrades | $25,000 | $29,000
New Office Building | $150,000 | $156,000
Total Estimated Costs | $1,375,000 | $1,556,000
<number>
Improvements | Current $ | Inflated $
Water Reclamation Plant | $650,000 | $686,000
Leach Field Expansion | $220,000 | $251,000
Pumping Trailer | $50,000 | $52,000
SCADA | $100,000 | $119,000
New Office Building | $150,000 | $156,000
Total Estimated Costs | $1,170,000 | $1,264,000
*Debt assumed for the sewer reclamation plant and the high elevation
water tank.

## Slide 14: Projected Revenue Requirement – WATER
<number>
Sufficient revenue collection this fiscal year

## Slide 15: Projected Revenue Requirement – SEWER
<number>
Insufficient revenue collection this fiscal year

## Slide 16: Projected District Cash Balances with Increased Rate Revenues
<number>
Target cash reserves = 3 months operating costs water & sewer plus 50% accumulated depreciation of assets in both systems
Per Prop. 218, only charging rates for revenue sufficiency

## Slide 17
Section III
Cost of Service
<number>
Notes: <number>

## Slide 18: Functional Cost Allocation - WATER
Customer Costs 26%
Capacity Costs 57%
Commodity Costs
Customer Charge = per Account (fixed)
Service Charge = per Meter (fixed)
Use Charges = per Thousand Gallons (variable)
<number>
Fixed Charges
Variable Charges
= 83%
= 17%
Fixed costs generally consist of costs incurred to serve customers irrespective of the amount or rate of water they use
Variable costs change in total as the volume of water consumption changes, as measured in a specific time period

## Slide 19: Functional Cost Allocation - SEWER
Customer Costs 30%
Capacity Costs 49%
Flow Costs 21%
Customer Charge = per Account (fixed)
Service Charge = per Connected and Unconnected EDU (fixed)
Flow Charge = per Connected EDU (fixed)
Each nonresidential account is assigned a number of EDUs based on wintertime water use. Unconnected lot accounts are assigned 1 EDU.
<number>

## Slide 20: Cost of Service
Water Costs
  Customer, Capacity, Commodity
    Customer costs divided by # accounts
    Capacity costs divided by equivalent meter units
    Commodity costs divided by estimated demand (gallons) – connected lots only
Sewer Costs
  Customer, Capacity, Flow
    Customer costs divided by # accounts
    Capacity costs divided by equivalent dwelling units
    Flow costs divided by equivalent dwelling units – connected lots only
  Unconnected Lots pay customer costs as well as capacity costs for 1 equivalent meter unit and 1 equivalent dwelling unit
Methodology ensures customer groups pay their proportional share of service costs

## Slide 21
Section IV
Rate Design
<number>
Notes: <number>

## Slide 22: Balance of Multiple Objectives
<number>

## Slide 23: Water Use by Customer Type (2019-2021)
<number>

## Slide 24: Single Family Monthly Use per Unit (EDU)
<number>
The average wintertime water use of a single family home is 115 gallons per day
Usage per EDU informs both the water and sewer rate designs

## Slide 25: Billable Accounts Projection
As of January 2022, the community is about 25% built.
R = Residential
CR = Commercial Residential
<number>

## Slide 26: Current Water Rate Structure
<number>
Fixed Charges | Use Charges
Connected Customers: Residential – Rate per Lot Non-Residential – Based on Meter Size Unconnected Lots: Assessment (Standby Fee) per Lot | Inclining rates per thousand gallons used Different blocks for residential and non-residential Residential 11 tiers, non-residential 3 tiers
Fixed Charges billed Quarterly; Use Charges billed Annually

## Slide 27: Developed Water Rate Structure
<number>
Fixed Charges | Use Charges
Customer Charge per Account Service Charge -- Residential Per Unit -- Non-Residential by Meter Size | All customers pay the same rate per thousand gallons consumed
Fixed Charges AND Use Charges billed Quarterly;
Assessments (Standby Fees) repealed
On and Off-Peak use rates were calculated but are not recommended as a) the seasonal cost difference is minimal and b) quarterly bills are not frequent enough to modify behavior

## Slide 28: Why Repeal (Standby) Assessments?
Better equity (cost of service) achieved if all costs are in the rates
If assessments are not updated, the connected lots subsidize the unconnected lots
Assessments cannot be increased without a 218 ballot – updating the assessments would double the District’s cost to achieve cost equity among customers
Per Government Code 54984.7- have to pass a resolution to collect the assessments each year (additional administrative cost)
<number>

## Slide 29: Removal of Tiers
<number>
Per California law, higher rates at higher consumption levels is only legal if the cost of service increases with greater consumption
Tiered rates not legally supportable
Average costs per gallon are lower during peak consumption period July-Sept; indicates that marginal cost analysis would not support tiered rates.

## Slide 30: Calculated Water Rates
<number>
[1] All water accounts with more than one Living Unit as of 6/1/2022 will only pay for one Living Unit until the property sells or is transferred to new ownership.
[2] Residential Lots with Additional Quarters pay for a maximum of two Living Units (Dwelling Unit plus Guest House). Commercial Residential Lots pay for every Living Unit.

## Slide 31: Calculated Sewer Rates
<number>
[1] Each Living Unit counts as one EDU. All sewer accounts with more than one Living Unit as of 6/1/2022 will only pay for one Living Unit until the property sells or is transferred to new ownership.
[2] Residential Lots with Additional Quarters pay for a maximum of two Living Units (Dwelling Unit plus Guest House). Commercial Residential Lots pay for every Living Unit.

## Slide 32
Section V
Customer Bill Impacts with
Cost of Service Rates
<number>
Notes: <number>

## Slide 33: Annual Impact to an Unconnected Lot
<number>

## Slide 34: Annual Utilities Bill Projection for a Typical Residence
<number>

## Slide 35: Comparison Utility Bills for a Home on a monthly basis
<number>

## Slide 36: Nonresidential Accounts Annual Bill Impacts based on fiscal year 2021 water use
<number>

## Slide 37
Section VI
Next Steps
<number>
Notes: <number>

## Slide 38: Next Steps
HEC prepares the Final Report with Board input
The Board sets the public hearing date
The Board directs staff and consultants to notify customers pursuant to Proposition 218
The Board appoints the General Manager and 1 or 2 Board members to approve the content and design of the Prop. 218 notice
<number>

## Slide 39: Timeline
<number>

## Slide 40: Proposition 218 Notice Required Elements
The public hearing date, time and place
The reason for the change in rates
The basis upon which the proposed rates were calculated
The proposed rates
Customer’s right to protest
A statement that a 120-day statute of limitations for challenging the rates applies once the new rates are effective (July 1, 2022)
<number>

## Slide 41: Customer’s Right to Protest
Every property owner has the right to protest the proposed rates included in the Proposition 218 notice
Only one protest per parcel can be counted*
Protest must be mailed or otherwise physically submitted in handwriting to the District – electronic submittals are invalid
A valid protest will be counted if received by close of the public hearing and it includes:
Customer’s name (must be legible)
Address or Assessor Parcel Number of the property
A statement of the rates being protested (water or sewer or both)
Signature and Date
*Protests must be filed with District records for a period of 2 years
<number>

## Slide 42: Adoption of New Rates
Upon close of the public hearing, the protests are counted separately for water and sewer.
If >50% of the owners of public record protest (separately for each utility), the Board cannot proceed.
Absent a majority protest, the Board can proceed with adoption of maximum rates.
At any time in the next 5 years, the Board can freeze or reduce the rates, but cannot increase them without another Proposition 218 public noticing process
<number>